# Raspberry Pi Light-Activated Keyboard
John Monigan

A "keyboard' that is played with a flashlight? Yup!
7 photoresistors are connected to a Raspberry Pi by an analog/digital converter. On the Pi, Java code sends MIDI signals to generate the tones corresponding to the "key". The light sensors are mounted in cylindrical holders to minimize "noise" from ambient light – the holders were designed in OpenSCAD and 3D printed.

## Parts
Raspberry Pi 2 Model B+ (512MB RAM)

- MCP3008 10 bit, 8 channel A/D converter
- GM55 photoresistors
- 3.3V voltage regulator (LM323)
- 100K ohm resistors

Use the flashlight to play a tune!
## Demo Notes

Username and password are just "pi"

The code is in and needs to be run from /home/pi/java

The command is ./run.sh net.monigan.pi.Play 50 1

The 2 arguments are:

50:	Number of milliseconds in delay in sense loop. 50 is conservative, 25 works but I haven't tested much.

1:	MIDI instrument number, 1 is piano.